## Slide 1: MEDCoupling Projection Methods & Parallelism
SALOME Training | Adrien Bruneton, Elie Saikali

## Slide 2: Agenda
Interpolation, extrapolation or projection?
Spatial discretization and nature of a field
What MEDCoupling can do for you
Parallelism in MEDCoupling

## Slide 3: Interpolation, extrapolation or projection?

## Slide 4: Illustration
Code coupling
Code A
Code B
??
A common technological problem
Spatial discretization from A
Spatial discretization from B

## Slide 5: Introduction
A typical use case: code coupling
  Different numerical codes simulate different physics
    And hence (might) use different numerical schemes
      E.g. temperature computed on nodes in code A and on elements in code B
    And/or different spatial discretization (i.e. different meshing of the same geometrical domain)
      A cylinder meshed with hexahedrons in code A, and with tetrahedrons in code B
    Or even worse, use different dimensions
      A heat flux on a 2D surface for code A and a 3D source term (e.g. fuel rode) for code B
  How do you “transfer” information from one to the other?
    I need to provide code B with the temperature computed by code A
    Solution A: ad-hoc solution. For each pair (code A, code B), write a mapper … good luck
    Solution B: use generic projection methods thanks to MEDCoupling 

## Slide 6: Projection, Interpolation?
Some vocabulary … or not
  Normally
    Interpolation: computing a function’s value at a given point inside a domain where the function’s values are known at discrete points
    Extrapolation: computing a function’s value outside a domain, but in relationship with points where the function’s values are known: hazardous!
    Projection: from linear algebra, expression of a function (a vector) into a new basis of a (another) vector space (often with a smaller dimension)
  Well, well, … in MEDCoupling, we do not take sides, and hence we
    Prepare the operation (given the two meshes)
    Transfer one or several fields (but apologies, sometimes you will still see interpolate or project)
  Fields on cells are called P0 fields
  Fields on nodes are called P1 fields (don’t ask me why)
  Two meshes are overlapping if they cover exactly the same spatial domain
  Temporal interpolation is not covered!

## Slide 7: A Trivial Example
In Python naturally 
  Transfer a field on cells onto a new field on cells
    import medcoupling as mc
    remap = mc.MEDCouplingRemapper()
    remap.setPrecision(1.e-12) # setting general options
    remap.prepare(srcMesh,trgMesh,”P0P0”) # cells to cells
    srcField.setNature(mc.IntensiveConservation) # nature of the field – see next...
    trgField = remap.transferField(srcField,1e+300) # default value to 1e+300
  srcField is a MEDCouplingFieldDouble
  srcMesh and trgMesh are MEDCouplingMesh-s

## Slide 8: Spatial Discretization & Nature Of A Field

## Slide 9: Spatial discretization of a Field
Where are the discrete values defined?
  A field can be supported by:
    The nodes (or vertices) of the mesh: ON_NODES  also called P1
    The cells (or elements) of the mesh: ON_CELLS  also called P0
    By more complex reference locations:
      Gauss Points (ON_GAUSS_PT, ON_GAUSS_NE),
      Kriging points (ON_NODES_KR)
  Obviously the projection methods will differ according to the localization
  Generally P0  P0 projection is the best supported option
    Source field is defined on cells
    Desired result: a target field expressed on cells
    Very common case
  Not all combinations are possible
    See the reference table at the end of the presentation
    If you don’t find what you need, ask for it!
P0
P1

## Slide 10: Field Nature (1/2)
Where physics comes into play
  A meaningful projection needs to know whether the physical quantity being projected is:
    Extensive: mass, power … quantity that scales with the volume of a cell
    Intensive: density, temperature … quantity that do not scale with the volume
  For each of the two above, two sub-methods are available, governing the behavior in case of non-overlapping meshes
    “Maximum” value preserved in the result
    “Integral” value preserved in the result
   see detailed formula in the documentation
  Invoke method: setNature() on the field
    If you don’t call it, no projection will be possible
  Possible argument values (warning different names prior to V8)
 | Intensive | Extensive
Conservation | IntensiveConservation | ExtensiveConservation
Maximum principle | IntensiveMaximum | ExtensiveMaximum

## Slide 11: Field Nature (2/2)
Example of non-overlapping mesh
  Understanding the problem of non-overlapping meshes:
  Take a look at the illustration right
    Mesh A in blue
    Mesh B in green
  For a projection from B to A, should:
    the full volume (here surface) of the cell from mesh A be taken into account?
      Knowing that only part of it coincides with the two cells in mesh B
    or only the volume covering both mesh A and mesh B?
      Letting aside what is not overlapping
    Depends on the nature of the physical quantity you’re handling
  Again, take a look at the full formulas + exercises:
    ${MEDCOUPLING_ROOT_DIR}/ share/doc/developer/InterpKerRemapGlobal.html#TableNatureOfField

## Slide 12: Functionalities

## Slide 13: Projection Methods
General principle
  To project one field onto a new target mesh, one has to:
  1.Prepare (required only once):
    The weight matrix is internally computed
      Ratios of the volumes between source cells and target cells
      From the source mesh and the target mesh only
      Wij: how much from source cell (i) will contribute to target cell (j)
      API: prepare(source, target, method)
  2.The source field must have a valid nature set!
  3.Transfer (can be done several times):
    A field on the source mesh can be transferred to the target mesh
      API: transfer(srcField, tgtField, defaultValue)
      Default value covers non-overlapping cases

## Slide 14: Supported configurations
What you can do
  Mesh combination (U: unstructured, C: cartesian, E: extruded)
    U  U
    U  C
    C  U
    C  C
    E  E
  Dimensions
    1D
    2D curve, full 2D
    3D surface, full 3D
  Spatial discretization
    P0  P0
    P1  P0
    P0  P1
    P1  P1
    P1  P0Bary
    PG  PG

## Slide 15: Parallelism

## Slide 16: Parallel Interpolation
Code name: DEC!
  Many codes today runs in « parallel »
    Here we cover inter-process exchange, MPI-like
  Still a need to exchange information between two parallel codes
    Simple transfer of information
    Or more complex projection as seen before
  Solution: Data Exchange Channels (DEC)

## Slide 17: ParaMEDMEM - OVerview
Where is the DEC used?
CAD
MESH
MESH
MESH
MESH
MESH
MESH
Code A
Code A
Code A
Code A
Code B
Code B
Mesh splitter
DEC
PARAVIS
Data reduction
Parallel meshing

## Slide 18: DEC – Step by step
The DEC step by step
  Objective
    Exchange data between two codes (yellow and purple) working on many sub-domains of the mesh
  Main objects in the DEC world: InterpKernelDEC and OverlapDEC
    InterpKernelDEC: code A and B run on separate procs
    OverlapDEC: code A and B share all the procs
  Algorithm
    1. Computation of bounding box per proc
    2. Exchanging the 2D sub-meshes potentially intersecting the domains
    Using the sequential Remapper (what we’ve seen before):
      3. Locate intersecting cells (BBTree)
      4. Compute pairewise contributions
    5. Final computation of the distributed weight matrix
P0
P1
P1’
P0’
P2’
P2
P3
P0
P1
P1’
P0’
P2’
P2
P3
P0
P1
P1’
P0’
P2’
P2
P3

## Slide 19: example
In C++ this time
InterpKernelDEC dec(boite_group, canal_group); // Field transfer example if (senderSide) {
MEDCouplingFieldDouble *f = T.getOutputField("vitesse_sortie"); dec.attachLocalField(f); dec.synchronize(); dec.sendData();
}
else if (receiverSide) { MEDCouplingFieldDouble*f = T.getInputFieldTemplate("vitesse_entree"); dec.attachLocalField(f); dec.synchronize(); dec.recvData(); T.setInputField("vitesse_entree",dec->getField()); }

## Slide 20: Conclusion

## Slide 21: Conclusion
Try it!
  Any question?
  Let’s go for the exercises!

## Slide 22: Direction Département Service
Commissariat à l’énergie atomique et aux énergies alternatives
Centre de Saclay | 91191 Gif-sur-Yvette Cedex
T. +33 (0)1 XX XX XX XX | F. +33 (0)1 XX XX XX XX
  Etablissement public à caractère industriel et commercial | R.C.S Paris B 775 685 019